Top of Form

| No: PUR/2011-12/IND19396 | Date: 28/11/2011 |
| --- | --- |

To

Sub : Request for Pro-forma Invoice Dear Sir This Research Institute is interested in purchasing of the items mentioned below. You are therefore requested to forward a pro-forma invoice along with your terms & conditions of supply & payment. Please provide a copy of the technical literature and the specifications of these items in a sealed envelope. Please read carefully the terms and conditions mentioned overleaf and submit your pro-forma invoice/quotation accordingly.

| SNo. | Name of Item | Catalog No | Qty |
| --- | --- | --- | --- |
| 1 | UltraSonicator for Bacterial Cell Disruption |  | 2 |

Important Please mention our reference number on the envelop and address all correspondence to Director IMT Chandigarh only. Please quote strictly as per our specifications. Please attach compliance sheet Proforma Invoice received after due date will not be considered under any circumstances. Please note that your Quotation should reach us latest by 17/01/2012 opened on 18/01/2012 Your Quotation must be duly stamped and reach directly to IMT from you only. If quotation is submitted by Indian representative/agent then they must have to produce a authority certificate of principal party for quotating the price Other wise it will be very difficult at our end to consider your quotation. EMD Rs ...... must be deposited along with quotation.

17/01/201218/01/2012

TERMS & CONDITIONS Commercial Cost : Mention the price of the material in the FOB/FCA including inland freight value only. Please note that being a Govt. Organization we cannot make Advance Payment. Cost of Packing, Forwarding, Freight, Transportation, Insurance charge may please be mentioned invariably, failing which offer is liable to be rejected. Agency Commission : Mention the percentage of Indian Agency Commission payable to commission Indian Agent in INR and also mention the name of your authorized Indian Agent/Representative, Pro-forma invoice without mentioning Indian Agency Commission will not be considered at our end. Validity : The validity of your pro forma invoice should be less than 180 days from the date of opening. Warranty : Mention the warranty period of equipment after satisfactory installation. 10% Bank Guarantee is to be submitted by you/your Agent for the Equipments costing Rs.25 Lac & above Taxes For Indigenous products, please quote Sales Tax/VAT/Service Tax/Freight/Other levies etc., if any, clearly in your quotation. General Condition Zerox copies of latest price list applicable list may be enclosed applicable in Indian Market. Ensure that quoted price will not be higher to any other customers in India to whom this particular item have been sold particularly to govt. of India Organization. Sent a certificate that the equipment is of latest technology & will not be obsolete within 5 years. Ensure that all essential spares parts of this equipment will available in India with your Indian Agent as and when required. Provide the list of the users in India of the same equipment along with their contact / email address. Enclose a copy of agreement with your authorized Indian Agent. FAX : 0091-172-2636683, 2690632 email : purchase@imtech.res.in TEL : 0091-0172-6665363 website : www.imtech.res.in

Yours faithfully,

Stores & Purchase Officer.

Specification for UltraSonicator for bacterial cell disruption

ULTRASONIC PROCESSOR

- Operating voltage: 220 V/50 Hz

- 500 – 750 watts, 20KHz

- Automatic tuning

- LCD screen with user prompts

- Program storage capability, 10 hour process timer

- Variable amplitude control

- Full function pulser – ON and OFF

- Overload protection circuit, remote actuation connector, quick disconnect

- Instruction manual

- Tool Kit

- Sound abating enclosure inside lined with white water proof noise abating material

- Support rod and clamp

- Laboratory Jack

- Probe with replaceable tip capable for processing volume between 10 to 50 ml

- Probe for processing the volume between 250 microlitre to 5 ml

Warranty: 3 years

Optionals

- Supplier should quote separately for five spare replaceable tips for probe used for processing volume between 10 to 50 ml.

- Temperature probe