Top of Form

| No: PUR/2011-12/IND21122/null | Date: 05/03/2012 |
| --- | --- |

To

Sub : Request for Pro-forma Invoice Dear Sir This Research Institute is interested in purchasing of the items mentioned below. You are therefore requested to forward a pro-forma invoice along with your terms & conditions of supply & payment. Please provide a copy of the technical literature and the specifications of these items in a sealed envelope. Please read carefully the terms and conditions mentioned overleaf and submit your pro-forma invoice/quotation accordingly.

| SNo. | Name of Item | Catalog No | Qty |
| --- | --- | --- | --- |
| 1 | Homogenizer, High Pressure |  | 1 |

Important Please mention our reference number on the envelop and address all correspondence to Director IMT Chandigarh only. Please quote strictly as per our specifications. Please attach compliance sheet Proforma Invoice received after due date will not be considered under any circumstances. Please note that your Quotation should reach us latest by 20/03/2012 opened on 21/03/2012 Your Quotation must be duly stamped and reach directly to IMT from you only. If quotation is submitted by Indian representative/agent then they must have to produce a authority certificate of principal party for quotating the price Other wise it will be very difficult at our end to consider your quotation. EMD Rs.60000/- must be deposited along with quotation. The quote must be under two bid system 1. Technical and 2.Price Bid

20/03/201221/03/2012

TERMS & CONDITIONS Commercial Cost : Mention the price of the material in the FOB/FCA including inland freight value only. Please note that being a Govt. Organization we cannot make Advance Payment. Cost of Packing, Forwarding, Freight, Transportation, Insurance charge may please be mentioned invariably, failing which offer is liable to be rejected. Agency Commission : Mention the percentage of Indian Agency Commission payable to commission Indian Agent in INR and also mention the name of your authorized Indian Agent/Representative, Pro-forma invoice without mentioning Indian Agency Commission will not be considered at our end. Validity : The validity of your pro forma invoice should be less than 180 days from the date of opening. Warranty : Mention the warranty period of equipment after satisfactory installation. 10% Bank Guarantee is to be submitted by you/your Agent for the Equipments costing Rs.25 Lac & above Taxes For Indigenous products, please quote Sales Tax/VAT/Service Tax/Freight/Other levies etc., if any, clearly in your quotation. General Condition Zerox copies of latest price list applicable list may be enclosed applicable in Indian Market. Ensure that quoted price will not be higher to any other customers in India to whom this particular item have been sold particularly to govt. of India Organization. Sent a certificate that the equipment is of latest technology & will not be obsolete within 5 years. Ensure that all essential spares parts of this equipment will available in India with your Indian Agent as and when required. Provide the list of the users in India of the same equipment along with their contact / email address. Enclose a copy of agreement with your authorized Indian Agent. FAX : 0091-172-2636683, 2690632 email : purchase@imtech.res.in TEL : 0091-0172-6665363 website : www.imtech.res.in

Yours faithfully,

Stores & Purchase Officer.

Homogenizer

Continuous homogenizer for biotechnology/ pharma applications with following specifications:

- High pressure (minimum 1500 bar) to break bacteria, yeast, algae, plant cells and particles present in fluid to the smallest particle size down to the nanometer range.

- Should consist of high quality stainless steel and high wear resistance materials,

pump valves: high wear resistance; pistons: tungsten carbide coated SS/solid ceramic

- Aseptic containment system, CIP/SIP cleanability, cGMP compliant system. The additional cost for cGMP certification, IQ/OQ/PQ documentation, if any, must be quoted as optional items.

- FDA approved gaskets and elastomers. Product contact materials and surface finish should be as per FDA regulations.

- Jacketed feed tank, SS 316L

- Flow rate: Minimum 35 L/h at 1500 bar

- PLC/ Microprocessor based control system, automated control system

- Capability for control over back pressure.

- Pressure control valves, actual pressure reading and indication system with high precision pressure gauzes.

- Built in safety protection against over pressure.

- Polished SS panels, sanitary tri-clamp connectors, adjustable anti-vibration feet.

- Accessory/ accessories for product cooling to be included and to be obtained as a part of the main equipment.

- Warranty: One year

Other conditions:

- The company must quote in foreign currency in case of imported system, in addition to Indian rupee (if the party so desires).

- cGMP certification/ documents and IQ/OQ/PQ documentation, if costs extra, to be quoted as optional items.

- List of Indian users (the original equipment manufacturer must have at least 5 installations of similar equipment in India) and satisfactory performance certificated from at least three Indian biotech/ pharma industries/ CSIR institutes/ IITs/ NIPER/ Central Universities to be attached.

- A certificate on technical/ service support from original equipment manufacturer for next 7 years to be submitted.

- A compliance statement for the quoted specifications vis-à-vis each of the above specifications supported by technical literature from original equipment manufacturer must be submitted.

- AMC for three years after completion of warranty period to be quoted.

Bottom of Form