Top of Form

| No: PUR/2013-14/IND28872/KK | Date: 26/09/2013 |
| --- | --- |

To

Sub : Request for Pro-forma Invoice Dear Sir This Research Institute is interested in purchasing of the items mentioned below. You are therefore requested to forward a pro-forma invoice along with your terms & conditions of supply & payment. Please provide a copy of the technical literature and the specifications of these items in a sealed envelope. Please read carefully the terms and conditions mentioned overleaf and submit your pro-forma invoice/quotation accordingly.

| SNo. | Name of Item | Catalog No | Qty |
| --- | --- | --- | --- |
| 1 | HPLC with UV & RI detectors, 1 |  | 1 |

Important Please mention our reference number on the envelop and address all correspondence to Director IMT Chandigarh only. Please quote strictly as per our specifications. Please attach compliance sheet Proforma Invoice received after due date will not be considered under any circumstances. Please note that your Quotation should reach us latest by 08/10/2013 opened on 09/10/2013 Your Quotation must be duly stamped and reach directly to IMT from you only. If quotation is submitted by Indian representative/agent then they must have to produce a authority certificate of principal party for quotating the price Other wise it will be very difficult at our end to consider your quotation. EMD Rs ...... must be deposited along with quotation.

08/10/201309/10/2013

TERMS & CONDITIONS Commercial Cost : Mention the price of the material in the FOB/FCA including inland freight value only. Please note that being a Govt. Organization we cannot make Advance Payment. Cost of Packing, Forwarding, Freight, Transportation, Insurance charge may please be mentioned invariably, failing which offer is liable to be rejected. Agency Commission : Mention the percentage of Indian Agency Commission payable to commission Indian Agent in INR and also mention the name of your authorized Indian Agent/Representative, Pro-forma invoice without mentioning Indian Agency Commission will not be considered at our end. Validity : The validity of your pro forma invoice should be less than 180 days from the date of opening. Warranty : Mention the warranty period of equipment after satisfactory installation. 10% Bank Guarantee is to be submitted by you/your Agent for the Equipments costing Rs.25 Lac & above Taxes For Indigenous products, please quote Sales Tax/VAT/Service Tax/Freight/Other levies etc., if any, clearly in your quotation. General Condition Zerox copies of latest price list applicable list may be enclosed applicable in Indian Market. Ensure that quoted price will not be higher to any other customers in India to whom this particular item have been sold particularly to govt. of India Organization. Sent a certificate that the equipment is of latest technology & will not be obsolete within 5 years. Ensure that all essential spares parts of this equipment will available in India with your Indian Agent as and when required. Provide the list of the users in India of the same equipment along with their contact / email address. Enclose a copy of agreement with your authorized Indian Agent. FAX : 0091-172-2636683, 2690632 email : purchase@imtech.res.in TEL : 0091-0172-6665363 website : www.imtech.res.in

Yours faithfully,

Stores & Purchase Officer.

Bottom of Form

TECHNICAL SPECIFICATIONS ANALYTICAL HPLC

1.            Solvent Delivery System for Analytical flow rates

- It should be High Pressure Binary Gradient two Pump System

- The flow rate should be 0.001 to 10 ml/min

- Flow rate precision should be less than (0.1% RSD

- Flow rate accuracy should be (1%

- Pressure setting range should be 1-40 MPa

- Maintenance kit, reservoir tray (with 2 solvent bottles complete with fittings)  & automatic rinsing kit must be supplied

- It must be capable of upgrading to low pressure Quaternary gradient operation if required.

- It must have a leak sensor as safety feature

- Gradient Mixer should be provided.

2.	UV-VIS Spectrophotometer Detector

- Light Source: Deuterium (D2)Lamp/Tungsten Lamp/ Halogen Lamp

- Wavelength Range: 190nm to 700 nm

- Band width, Slit width: 8 nm

- Wavelength precision: ± 0.1nm

- Wavelength accuracy: ± 1.0 nm

- Noise: +0.25X10 -5 AU (0.5x10 -5 AU)

- Drift : 1x10-4 AU/hour

- Cell: Optical wavelength: 10mm, Capacity: 12 UL , withstand pressure: 12MPa

3.	Sample Injectors :

Rheodyne Manual with 20 ul loop, Mounting Plate and syringes 25 ul, 250 ul.

4.           Refractive Index Detector

- Refractive Index range : 1-1.75 RIU

- Noise Level should be less than 2.5 x 10-9 RIU

- Drift should be less than 1 x 10-7 RIU/hour

- Range : A mode : 0.01-500 x 10-6 RIU

P and L modes: 1 - 5000 x 10-6 RIU

- Response : 0.05-10 seconds, 10 step selection

- Zero point adjustment : Auto, Auto optical, and Fine

- Flow Cell Volume : 9 uL

- Ambient Temp. : 4-35 Deg. C

- .  	Computer and Software

- All in one Desktop system with i 7 processor, 8GB RAM, 00 GB hard Disk, Microsoft office, windows 7 compatible operating system.

- It should cover full one-point digital instrument control, qualitative and quantitative processing, report creation and self-diagnosis

- The software should allow automatic execution of system checks, auto-purge and baseline checks

- Sample schedule wizard function should be standard

- There should be an on-line help function context sensitive

- System suitability, System security as well as System check functions must be provided which comply with Good Laboratory Practice (GLP) and Regulatory Conformity

6.	Installation and Operational Qualification (IQ/OQ) Quoted separately

7. 	Warranty:  minimum two years of standard warranty should be quoted