| No: PUR/2009-10/IND11306/KK | Date: 23/11/2009 |
| --- | --- |

Sub : Request for Pro-forma Invoice Dear Sir This Research Institute is interested in purchasing of the items mentioned below. You are therefore requested to forward a pro-forma invoice along with your terms & conditions of supply & payment. Please provide a copy of the technical literature and the specifications of these items in a sealed envelope. Please read carefully the terms and conditions mentioned overleaf and submit your pro-forma invoice/quotation accordingly.

| SNo. | Name of Item | Catalog No | Qty |
| --- | --- | --- | --- |
| 1 | Fluorescence microscope , 1 |  | 1 |

Important Please mention our reference number on the envelop and address all correspondence to Director IMT Chandigarh only. Please quote strictly as per our specifications. Please attach compliance sheet Proforma Invoice received after due date will not be considered under any circumstances. Please note that your Quotation should reach us latest by 14/12/2009 opened on 15/12/2009 Your Quotation must be duly stamped and reach directly to IMT from you only. If quotation is submitted by Indian representative/agent then they must have to produce a authority certificate of principal party for quotating the price Other wise it will be very difficult at our end to consider your quotation. EMD Rs ...... must be deposited along with quotation. Quotation must be submitted in two Bid System 1) Technical Bid 2) Price Bid

14/12/200915/12/2009

Yours faithfully,

Stores & Purchase Officer.

SPECIFICATIONS FOR FLUORESCENCE MICROSCOPE

|  | SPECIFICATIONS |  |
| --- | --- | --- |
| 1. | MICROSCOPE STAND | ERGONOMIC DESIGN UPRIGHT MICROSCOPE BODY WITH BUILT-IN COLOR /LIGHT BALANCE FILTERS |
| 2. | OPTICAL SYSTEM | INFINITY CORRECTED OPTICAL SYSTEM |
| 3. | EYEPIECE LENS | 10X (2PCS) BOTH WITH DIOPTER ADJUSTMENT (F.O.V. 25MM OR BETTER) |
| 4. | OBJECTIVES | HIGH N.A. PLAN APOCHROMATIC OBJECTIVES FOR ~4X, ~10X (N.A. 0.3), ~20X N.A. 0.5), ~40X N.A. 0.75), 60/63X WATER N.A 1.3 PREFERABLY 1.4 &100X OIL N.A. 1.3) HIGHER NA PREFERRED. ALL OBJECTIVES SUITABLE FOR HIGH RESOLUTION FLUORESCENCE WORK AND IT SHOULD BE CAPABLE OF DIC WORK. |
| 5. | NOSE PIECE | REVOLVING NOSEPIECE TO ACCOMMODATE AT LEAST SIX OBJECTIVES AT A TIME |
| 6. | STAGE | X AND Y RECTANGULAR MECHANICAL STAGE MOTION CONTROL ON RIGHTHAND SIDE, |
| 7. | CONDENSER | UNIVERSAL CONDENSER |
| 8. | ILLUMINATION | 12V, ATLEAST 100W OR BETTER HALOGEN ILLUMINATION |
| 9. | FLUORESCENE ATTACHMENT | EPIFLUROSCENCE CAPABILITY 100W/120W/130W MERCURY FIBER LIGHT ILLUMINATOR WITH LAMP. OR METAL HALIDE ILLUMINATOR, BOTH WITH VARIABLE INTENSITY OUTPUT. SHOULD HOLD AT LEAST 6 FLUORESCENCE FILTER BLOCKS SINGLE BANDPASS FILTER BLOCKS FOR UV, BLUE &GREEN EXCITATION, 2 ADDITIONAL EXCITATION FILTERS ALONG WITH SUITABLE DICHORICS FOR i) EXCITATION ~ 400-415nm, ii) EXCITATION IN RED DYES LIKE ALEXA 633, OR EQUIVALENT ) |
| 10. | DIGITAL CAMERA | HIGH RESOLUTION DIGITAL COLOR AIR COOLED CCD CAMERA CAPABLE OF HANDLING VERY LOW LIGHT FLUORESCENCE & BRIGHT FIELD IMAGES WITH AT LEAST 0.5” HIGH DENSITY CCD CHIP, AT LEAST1.4 MEGAPIEXELS RESOLUTION |
| 11. | SOFTWARE | FOR IMAGE ACQUISTION, TIME LAPSE IMAGING, MULTI-CHANNEL FLUORESCENCE, ANNOTATION, MORPHOLOGY/MORPHOMETERY, AUTO-MEASUREMENT, OVERLAY, SPOT METERING CAPABILITY. |
| 12. |  | MICROSCOPE, CAMERA & SOFTWARE PREFERABLY FROM SAME MANUFACTURER FOR BETTER COMPATIBILITY. |
| 13. | Spares | AT LEAST THREE SPARE HG/METAL HALIDE LAMPS AND THREE SPARE HALOGEN LAMPS. FULL STARTER KIT WITH IMMERSION OIL (AT LEAST 100ML X 3) FULL FILTER SET AND LENS PAPER PACK. |
| 14. | DATA COLLECTION AND PROCESSING UNIT (LOCALY SUPPLY) | BRANDED (LATEST) WITH AT LEAST 4 GB RAM, DVD WRITER, 500 GB OR HIGHER HDD, 19”TFT MONITOR ALONGWITH UPS |
| 15. | Accessories | VIBRATION FREE TABLE, TWO ERGONOMIC CHAIRS FOR STRESS FREE OPERATION AND LIGHT ISOLATION CHAMBER. |
| 16. | OPTIONAL | PLAN APO OIL OBJECTIVE LENS ~150X OR INTERMEDIATE MAGNIFICATION CAPABILITY FOR MICROBIAL SPECIMENS. STAGE HOLDER FOR PETRI DISHES. |

TERMS & CONDITIONS

Commercial

1) Cost                  : 	Mention the price of the material in the FOB/FCA including inland freight value only. Please note that being a Govt. Organization we cannot make Advance Payment.

2) Insurance         :	Consignment should be insured through National Insurance               Company of India or is associate in your country.

3) Freight              :	The dispatch of the material should be through Air India preferably.

4) Agency             : 	Mention the   percentage   of   Indian   Agency Commission payable  to

Commission            commission Indian Agent in INR and also mention the name of your   authorized Indian Agent/Representative, Pro-forma invoice without mentioning Indian Agency Commission will not be considered at our end.

5) Validity             : 	The validity of your pro forma invoice should be less than 180 days from the date of opening.

6) Warranty           : 	Mention the warranty period of equipment after satisfactory   installation. 10% Bank Guarantee is to be submitted by you/your Agent for the Equipments costing Rs.25 Lac & above

General Condition

- Zerox copies of latest price list applicable list may be enclosed applicable in Indian Market.

- Ensure that quoted price will not be higher to any other customers in India to whom this particular item have been sold particularly to govt. of India Organization.

- Sent a certificate that the equipment is of latest technology & will not be obsolete within 5 years.

- Ensure that all essential spares parts of this equipment will available in India with your Indian Agent as and when required.

- Provide the list of the users in India of the same equipment along with their contact / email address.

- Enclose a copy of agreement with your authorized Indian Agent.

FAX : 0091-172-2690056, 2690632			                                   email : purchase@imtech.res.in

TEL  : 0091-0172-2690056, 2636680 - 94     	                                            website : www.imtech.res.in