| No: PUR/2009-10/IND12002 | Date: 19/02/2010 |
| --- | --- |

To Sub : Request for Pro-forma Invoice Dear Sir This Research Institute is interested in purchasing of the items mentioned below. You are therefore requested to forward a pro-forma invoice along with your terms & conditions of supply & payment. Please provide a copy of the technical literature and the specifications of these items in a sealed envelope. Please read carefully the terms and conditions mentioned overleaf and submit your pro-forma invoice/quotation accordingly.

| SNo. | Name of Item | Catalog No | Qty |
| --- | --- | --- | --- |
| 1 | Electrochemical Analyzer with necessary software and accessories, 1 |  | 1 |

Important Please mention our reference number on the envelop and address all correspondence to Director IMT Chandigarh only. Please quote strictly as per our specifications. Please attach compliance sheet Proforma Invoice received after due date will not be considered under any circumstances. Please note that your Quotation should reach us latest by 09/03/2010 opened on 10/03/2010 Your Quotation must be duly stamped and reach directly to IMT from you only. If quotation is submitted by Indian representative/agent then they must have to produce a authority certificate of principal party for quotating the price Other wise it will be very difficult at our end to consider your quotation. EMD Rs ...... must be deposited along with quotation.

Yours faithfully,

Stores & Purchase Officer.

Electrochemical analyzer (workstation) (220V/50Hz) capable of doing analysis with following major techniques

- Cyclic Voltammetry (CV) and Linear Sweep Voltammetry (LSV)

- Chronoamperometry (CA),  Chronopotentiometry (CP), Chronocoulometry (CC), Repeating Chronoamperometry and  Chronopotentiometry

- Normal and Differential Pulse Voltammetry  with stripping

- Square Wave Voltammetry  with stripping

- AC Voltammetry  and Second Harmonic AC Voltammetry

- Amperometric I-t Curve

- Differential Pulse Amperometry and Double  Differential Pulse Amperometry

- Integrated pulse Amperometric Detection

- AC Impedance

- Impedance – Time and Potential

- Multi-Current Steps

- Potentiometric Stripping Analysis

- Galvanostat

Specifications:

Potentiostat : CV and LSV scan rate: 0.00001 to 5000 V/s or better

Max Current: ( 250 mA or higher

Current resolution : < 0.1 pA

Compliance voltage: ( 12 V or higher

Potential increment: 100 (V or lower

Input impedance of electrode: > 1012 ohm

Input bias current: <50  pA

Common mode rejection ratio: > 50 dB (1 MHz)

Sensitivity scale: (10-12 in different ranges

Analog/Digital converters: 16 bits or higher

Serial and USB ports for data communication

Cell control: purge and stir

Essential accessories:

# Electrochemical Cell System includes 4 glass cells with one Cell top

2mmPt Working Electrode: minimum   5 pkg

3mm GC Working Electrode: 5 pkg

Ag/AgCI Reference (aq):  5pkg

Ag/AgCl Reference (non aq): 5pkg

Calomel Reference Electrode

Pt Wire Counter Electrode

Electrode Polishing Kit

State-of-art fully compatible computer system (minimum configuration: high speed core 2 duo processor,  4 GB SDRAM; 360 GB HDD; graphic card, 19” LCD monitor etc.) with LASER printer and necessary Windows Based Acquisition Software (framework software), Interface Cable (Serial / USB), Universal cell with necessary cell cable and the system operating manuals

### Service warrantee: 2 years on complete system

Optional accessories:

8 channel multiplexer (upgradeable to 32 channels or more)

Dr. Bob’s Cell kit with standard cell

TERMS & CONDITIONS

Commercial

1) Cost                  : 	Mention the price of the material in the FOB/FCA including inland freight value only. Please note that being a Govt. Organization we cannot make Advance Payment.

2) Insurance         :	Consignment should be insured through National Insurance               Company of India or is associate in your country.

3) Freight              :	The dispatch of the material should be through Air India preferably.

4) Agency             : 	Mention the   percentage   of   Indian   Agency  Commission payable  to

Commission              commission Indian Agent in INR and also mention the name of your   authorized Indian Agent/Representative, Pro-forma invoice without mentioning Indian Agency Commission will not be considered at our end.

5) Validity             : 	The validity of your pro forma invoice should be less than 180 days from the date of opening.

6) Warranty           : 	Mention the warranty period of equipment after satisfactory   installation. 10% Bank Guarantee is to be submitted by you/your Agent for the Equipments costing Rs.25 Lac & above

General Condition

- Zerox copies of latest price list applicable list may be enclosed applicable in Indian Market.

- Ensure that quoted price will not be higher to any other customers in India to whom this particular item have been sold particularly to govt. of India Organization.

- Sent a certificate that the equipment is of latest technology & will not be obsolete within 5 years.

- Ensure that all essential spares parts of this equipment will available in India with your Indian Agent as and when required.

- Provide the list of the users in India of the same equipment along with their contact / email address.

- Enclose a copy of agreement with your authorized Indian Agent.

FAX : 0091-172-2690056, 2690632		                      email : purchase@imtech.res.in

TEL  : 0091-0172-2690056, 2636680 - 94     	                          website : www.imtech.res.in